## Slide 1: BOM Upload and Verification
VSM
Value Stream Mapping
Rev 1.1
Updated 9th June 2021

## Slide 2: Initial Discussions
Go through the steps involved and find obvious bottlenecks and risks
  Step 1: Get the data – BOM and QCW (Including Labour and Materials Quote)
    BOM received by email from PM
    QCW received by email from PM
    Waiting time between request and receive
      PE should have access to the ‘source’ and get themselves these files
        QCW – is loaded in the RFQ DB
        PE to get access to RFQ DB to get the QCW
        Data pack (including the BOM) should be loaded in newly created NPI DB and BOM can be downloaded from there when needed
        Current alternative storage location for the data pack is S:\PRODENG folder
        On top of that other folders are used by other departments for storing data packs – risk of mixing up info and retrieving wrong revisions

## Slide 3: Initial Discussions
Separate Note regarding RFQ process:
  Often bare PCB is quoted with minimalistic panelisation features and is not following ‘SRX Panelisation Guideline’ shared with our suppliers
  Often PCB is quoted one per (not panelised)
    Need to find the optimum way to communicate to the quote team the desired panelisation size and number of boards per panel
  Finalise PCB quote should be shared with PE for approval/validation before is loaded in the QCW
  Otherwise we end up in the situation when we get a very cheap price during RFQ and then when we place the order price is changed due to the fact that basically the panelisation and features required for manufacturing are added only at this point. It changes the BOM price and making us lose money or go back to the customer at this late stage and ask for cost increase and amended PO.
  Too many alternative MPNs are quoted during the RFQ, especially the ones under Consolidation category, which are our decision to change customer BOMs due to our supply chain arrangements
    All these alternative MPNs need to be approved by the customer before we can upload them in the system
    They make BOM upload process much slower
    Need to review the “Consolidation” category justification and rules of engagement
    During the RFQ customer MPN should be quoted first and then the alternative should be added if alternative is a better option (better availability and price)
    In the Quote Letter should be presented the price following the customer BOM/MPN and an alternative price (lower) that could be achieved if customer wants to get involved in approving a number of alternative

## Slide 4: Initial Discussions
Step 2: Data check
  Customer BOM is checked against quoted BOM (from QCW)
  BOM Comparison
    Rev Check
    MPN, Ref Des, Qty check
      BOM Comparison done manually in Excel
      Not Standardised – each PE has his own way of doing it – adds the risk of not capturing all the time all the possible issues
      Time Consuming
    Need to investigate if BOM Comparison tool can help comparing the customer BOM and the QCW BOM
    Alternative solution – improve and standardise the EXCEL comparison (template, macros)
    Organise external EXCEL training for PE to improve the skills and offer a better understanding of the enhanced Excel features/functions
    Alternative solution – create web-based application for BOM Comparison with easy-to-follow functions for BOM upload and highlight the differences
    Alternative solution – Use Valor MSS BOM Compare Tool – Train Engineers how to use it
    Trial BOM Connector tool from Siemens – it links with Valor MSS and possibly Movex

## Slide 5: Initial Discussions
Step 3: Decide which parts need new PN to be created in Movex
  New BOMs usually mean new part numbers to be created in the system, but system (Movex) need to be checked first to avoid duplication – for the same customer create a new PN for an MPN that already has a Movex PN
  Movex check is done manually in Excel
    Need to download the parts that are already created for that customer – report called Customer Part Mapping
    Report needs to be reformatted before can be compared with the new BOM
    Check is done based on Customer Part Number (Alias) if available or MPN and Manufacturer
      Comparison done manually in Excel
      Not Standardised – each PE has his own way of doing it – adds the risk of not capturing all the time all the possible issues
      Time Consuming
    It will help if QCW has also a consolidated BOM, in case of multiple BOMs upload for a customer. It could be organised as a Pivot Table
    Parts that Match (PN already in the system) don’t require any new PN
    Partial Match – some of the MPNs are matching an existing Movex PN, but not all
      Requires further work and Customer approval or a new PN must be created
      Manual, time consuming work (download, email, explanations)
    No Match – a new PN must be created

## Slide 6: Initial Discussions
Step 4: ECN - Create SRX PN & Stock Code – need SRX PN, Desc, Status, ECN No, ECN Line
  Each PN has a certain format like LF-if is lead-free, XX-customer code like RM, XX – commodity code and XXXX- 4 digits incremental number
  LFRM120008
  PE must find, manually, the right commodity code based on MPN description or checking the Data Sheet
  PE must find, manually, the last PN allocated for that customer and that commodity and pick the next available number for the new PN that will be created
  Description of the SRX PN must be MAX 30 characters otherwise Movex won’t accept it
  Template & QCW including the SRX PN column must be sent by email to Procurement to add Procurement parameters
  UOM once created can't be changed, if is wrong a new PN must be created
  All the templates need to be saved as Text(Tab Delimited) otherwise upload fails
  Stargile – doesn’t have any error checking mechanism
  All Stargile issues have been centralised in WIKI

## Slide 7: Initial Discussions
STEP 5 – ECN – Routing Upload
  PE needs to get from PM the batch quantity in order to load the right routings
  Movex doesn’t support multiple routings for the same BOM
  If Batch QTY changes then routings need to be updated
Step 6 – ECN – BOM Upload: PN, QTY, Designator, Operation Number
  Operation numbers used:
    50-SMT
    100-TH
    160-Mechanical
    190-Packing
  By this stage you need to know which parts are SMT, TH, Mechanical, Packing – at this stage manual search no automatic scripts or help
  Reference Designators will be available in Movex Reports only next day – updating scripts introduce by IT at 10AM, 2PM, 6PM to shorten the wait
  Add manually the Rev Data in Movex
  QTY difficult to be determined at BOM upload stage for glues, conformal coating and other consumables
  All the templates need to be saved as Text(Tab Delimited) otherwise upload fails
  Stargile – doesn’t have any error checking mechanism
  All Stargile issues have been centralised in WIKI

## Slide 8: Initial Discussions
Step 7 – ECN MPN Uploads (different template): PN, MPN, Manufacturer (30), Manufacturer Code
  Manufacturer and Manufacturer Code – manually searched and updated in the template
  Is Manufacturer Code used anywhere? Can we eliminate it?
  Currency is also a mandatory field which is not used – by default PE put AUD
  All the templates need to be saved as Text(Tab Delimited) otherwise upload fails
  Stargile – doesn’t have any error checking mechanism
  All Stargile issues have been centralised in WIKI
Step 8 – Check the Movex BOM against customer BOM
  Download BOM from Movex
  Compare against customer BOM
    Comparison done manually in Excel
    Not Standardised – each PE has his own way of doing it – adds the risk of not capturing all the time all the possible issues
    Time Consuming
  Can we create a new Crystal report that has PN with multiple MPNs on multiple lines?
  Is BOM Comparison Tool still working? Can it be used to simplify this step?
  Can we organise External EXCEL Training to improve PE Excel skills?
  BOM is also send to customer to verify
    Some customers are checking it, some don’t
    Some customers have advanced tools for BOM check – we need something similar
  Trial BOM Connector tool from Siemens – it links with Valor MSS and possibly Movex

## Slide 9: Initial Discussions
Step 9 – Optional – Purge
  Purge is still done on paper – time consuming – database could simplify the process
  Purge Template – end date for MPN doesn’t work – escalate to Karen and John B
Step 10 – Transmittal for PCB and Mechanical parts (build by drawing)
  All the Gerbers and drawings are uploaded in DMR
  Signed Transmittals are kept on S Drive
  Transmittals are requested and sent manually (PE asking Thu) or picked up by QA from the ECN
  Manual search for Supplier Number to be added on Transmittal
  Notes are added in Transmittal for PCBs regarding panelisation
  Transmittal should have a database to be able to check/find what was sent, when, by whom, etc.

## Slide 10: Initial Discussions
Step 11 – Upload BOM in MTS
  BOM downloaded from Movex and uploaded in MTS?
  Can it be transferred automatically?
Step 12 – Create routings, process flow in MTS

## Slide 11: Stargile (ComActivity) Issues & Improvement Suggestions
GENERAL
Stargile only works properly in Windows Internet Explorer 9 (very old version!). Needs update to work in latest browsers.
ECN RELATED
Would be good if we can create some pre-set process configurations and distribution lists based on the type of ECN changes. Currently relying on initiator to select the right roles and enter the right names for every ECN one by one.
Process configuration and distribution list should be customizable. Eg, there are two mandatory doc control approvals which is not necessary and just adds delays to ECN implementation.
There is no validation between the names entered in Distribution List and the roles ticked in Process Configuration and vice versa. If a process is ticked but no name entered against the role the ECN goes to a random person. Vice versa if a name is entered but role not ticked then that person will never receive the ECN. Very EASY TO MAKE MISTAKE!
Need to be able to upload files directly into an ECN (such as approvals, e-mails, working files, etc). Currently we have to upload in DMR and then type the path into the ECN so that people can find the related files.
In View BoMs there is no validation when a duplicate sequence number is entered in a new BoM upload, or BoM update. If you have duplicate sequence in a BoM upload, Stargile will only load one of the line items with a mixture of part number and circuit references from the two separate lines – THIS MEANS WE CAN MISS TO ORDER A REQUIRED COMPONENT.
View BOM, MPN, ITEM, ROUTES buttons should be highlighted when there is information entered in them.
Bom Revision and ECN Text in PDS001 not in Stargile has to be updated manually.
Cannot delete customer Alias number via ECN, can only add additional Alias. If want to delete have to do in Movex.
Add extra columns to the ecn “View Items” summary screen – “Name” “Purchase Price” and “Currency”.
If two ECN’s created at same time affecting same p/n in same bom there is no warning message. If both ECN’s are at a status prior to 50 only one of the updates will take affect.
Uploading items works even on ECN that is at status 95 – Complete Also it lets you delete line items from the ECN even after Movex update is done.
In View Items it does not retain the old information of the change. The fields on the right should show what was before, and the left what is the new information. All the fields just display whatever is the latest information in Movex after ECN is completed. so there is no history of the changes.

## Slide 12: Stargile (ComActivity) Issues & Improvement Suggestions
. ECR Implementation Schedule needs to be customizable, or at least we need CommActivity to update to add the following checks:
  AOI programs to be updated.
  New wave pallets required?
  MES update required?
  Valor MSS update required?
Separate ECN’s required to create new items, upload routes, upload BoM & MPN. It would be good if all can be done in one ECN, as it adds a lot of delay and processing time to some basic BoM updates.
When adding MPN’s the “currency” field is mandatory even though we don’t use it. Please make it non-manadatory as it’s waste of time entering data there.
When adding MPN’s we have to enter the Movex manufacturer code, as well as the manufacturer name. Should be one or the other as it wastes time to do both. The manufacturer code could be linked to Movex to display the name automatically.
MAINTENANCE RELATED
Can we have a customizable view’s that show all information we need in one page. eg. would be good to have one view that displays Part Number, Description, Manufacturer, MPN, Stock On Hand.
Would be good to have more fields for MPN updates such as:
  Shelf life
  Packaging (eg. Tape & Reel, Tube, Tray, Bulk, etc.)
  EOL, Obsolete Status
  YEOL – Years to EOL
  Do Not Buy / Not Preferred status
  NRND – Not recommended for new designs
  MSL (Moisture Sensitivity Level)